## Slide 1: 3d-Printed Granular Jamming Hand
Melissa Indoe
Chris Kang
Sean Phelan
Maggie Serra
Chris Wallace

## Slide 2: State-of-the-Art Designs
bebionic3 Hand – used as human prosthesis
Individual Motors in each finger. The motors are positioned to optimize weight distribution, making the hand feel lighter and more comfortable.
14 Selectable grip patterns and hand positions
Proportional Speed Control gives you precision control over delicate tasks, so you can pick up an egg as easily as crushing an empty can.
Durable construction and advanced materials makes
bebionic3 strong enough to handle up to 45kg
Selectable thumb positions
Innovative palm design protects bebionic3
from impact damage, and makes the hand
quieter than ever.
Soft finger pads that enhance grip.

## Slide 3: State-of-the-Art Designs
i-limb ultra revolution – used as human prosthesis
Powered rotating thumb
Five independently articulating digits with individual stall out ability. Each finger bends at the natural joints
A variety of flexible wrist options enabling more natural movement
New remote electrodes are
waterproof, lower profile,
and gold-plated for higher
sensitivity
Battery powered

## Slide 4: Existing Designs
RoboHand
Completely 3D printed except for three components
Bend wrist down to close fingers
Bend wrist up to release grip
Designed for people with no fingers

## Slide 5: Existing Designs
InMoov
3D printed by a hobbyist
Uses motors and sensors

## Slide 6: Granular Jamming
Coarse substance in a
flexible casing is soft
until air is removed
This can be used to
pick up or grip objects

## Slide 7: Granular Jamming In Action

## Slide 8: Deliverables at end of Semester
Gain significant knowledge in the materials and robotics field
OpenSCAD will be used to create a complete prototype of the device in Phases II and III.
Finalized Bill of Materials
Understand and address the impact of the design in ethical, environmental, social, political, health and safety, sustainability, standardization/standards context

## Slide 9: Conceptual Designs
To simplify the design process, brainstorming was split into categories:
  Category 1: Hand Ideas
    Ideas relating to the rigid components of the hand
  Category 2: Granular Jamming Ideas
    Ideas relating to the granular jamming pads
  Category 3: Other Considerations
    These were ideas or requirements that did not fit into any one category

## Slide 10: Hand Ideas
Joint ideas
  Ways to move joints
    Pneumatics
    Motors (one per joint)
    Cables
      One cable per finger
      One cable per finger, share cable for ring and pinky
      One cable per joint per finger
      One cable for 2 joints per finger
    Motors and cables (motors at finger base)
  Ideas to hold position
    Gear teeth at joint interface
    External joint locks

## Slide 11: Hand Ideas (continued)
Straightening out the hand
  Long rubber bands
  Dental rubber bands
  Flat springs
  A second set of cables
Sensing grip
  No grip sense: vacuum activated by button
  Place bump sensor under granular jamming pad
  Place encoder on servo motor, see if servo is stalled

## Slide 12: Joint Ideas Decision Matrix
Category: | Simplicity | Affordability | Size | Range of Motion | Totals:
Category Weight: | 10 | 8 | 10 | 8 | 
Item: |  |  |  |  | 
Pneumatics | 2 | 4 | 3 | 6 | 130
Motors (1/joint) | 1 | 1 | 1 | 10 | 108
Cables | 9 | 9 | 9 | 7 | 308
Motors & Cables | 6 | 7 | 5 | 8 | 230

## Slide 13: Cabling Ideas Decision Matrix
Category: | Simplicity | Affordability | Range of Motion | Totals:
Category Weight: | 10 | 8 | 8 | 
Item: |  |  |  | 
5 Cables (1/Finger) | 9 | 9 | 7 | 218
4 Cables | 9 | 10 | 5 | 210
1 Cable/Joint | 2 | 2 | 9 | 108
1 Cable/2 Joints | 4 | 4 | 8 | 136

## Slide 14: Hand Straightening Ideas Decision Matrix
Category: | Simplicity | Affordability | Reliability | Repairability | Range of Motion | Totals:
Category Weight: | 10 | 8 | 7 | 6 | 8 | 
Item: |  |  |  |  |  | 
Long Rubber Bands | 8 | 9 | 4 | 2 | 7 | 248
Dental Rubber Bands | 6 | 9 | 5 | 9 | 7 | 277
Flat Springs | 8 | 6 | 9 | 5 | 7 | 277
Second Set of Cables | 4 | 2 | 8 | 7 | 9 | 226

## Slide 15: Grip Sense Decision Matrix
Category: | Simplicity | Affordability | Reliability | Repairability | Usability | Totals:
Category Weight: | 10 | 8 | 7 | 6 | 10 | 
Item: |  |  |  |  |  | 
Vacuum Button | 9 | 9 | 9 | 9 | 1 | 289
Bump Sensor | 4 | 4 | 3 | 2 | 10 | 205
Encoder Boards | 8 | 8 | 8 | 8 | 9 | 338

## Slide 16: Granular Jamming Ideas
HI CHRIS

## Slide 17: Project Background and Problem Statement
Mechanical hands have existed for years
  Inaccurate motions
  Poor ability to grasp irregularly shaped objects

## Slide 18: Societal Impact
Prosthetic
Manufacturing and automation
Handling of dangerous materials
Open source

## Slide 19: Features of Design – Granular Jamming
Jamming –a physical process by which some materials, such as granular materials become rigid with increasing density.
Notes: When particles are not jammed, they are able to flow past each other. When jammed, the group of particles becomes more rigid, like how sand can be poured, but is still able to support your weight when you stand on it.
The planned design will make use of this by having pads of granular material along the palm of the hand, and then forcing the granules to jam by sucking the air out of the sac.

## Slide 20: Conceptual Design Comparison
Layout of Granular Jamming Pads
Pad in each length
Pad in first and third length

## Slide 21: Conceptual Design Comparison
Connecting jamming pads to vacuum
  Each pad has a tube to the vacuum
  Pads have connections to each other

## Slide 22: Other Considerations
Polycarbonate plastic
  Making the product out of polycarbonate plastic means that it will be much stronger than most available 3d printed plastic
Use with touch screens
  Conductive fabric can be added to the index finger and thumb to allow its use with smartphones
Nails
  Nails are used for certain tasks (such as opening bottles)
  Adding prosthetic “nails” to the project will add a little functionality
Size
  Hand must follow roughly the same size of a real human hand, and cannot be much heavier

## Slide 23: Hand Size
Important to match size of an average hand
Hand segment lengths (middle finger):
  L1 = 44.6 mm
  L2 = 26.3 mm
  L3 = 17.4 mm
  Ltip = 3.95 mm
  Lpalm = 88.2 mm
Palm Width = 79 mm
Finger Width= 19.75 mm

## Slide 24: Hand size (continued)
Weight of the hand = 425.7 g
Weight of hand & forearm = 1,699.1 g
Finger length ratios:
  Index = 0.8*(Middle Length)
  Ring Length = 0.93*(Middle Length)
  Pinky Length = 0.74*(Middle Length)

## Slide 25: Conceptual Design
Primary hand design:
  Run by 5 cables attached to motors in the forearm
  Hand will be kept straight via dental rubber bands or flat springs
    (If there is time, both will be tested)
  Grip will be sensed via encoders tracking each motor
  Emulate the size and weight of an average human hand
Secondary goals:
  Wrist motion
  Locking joints
  Use with touchscreens
  Accurate finger length ratios
  Nails

## Slide 26: Technical Analysis
Real hand motion
3 degrees of freedom
  Supination/pronation
  Extension/flexion
  Ulnar deviation/radial deviation

## Slide 27: Technical Analysis
2 degrees of freedom
Twist and extension/flexion

## Slide 28: Engineering Design
Motors for fingers
A digital I/O for signals from sensors and motors
Granular jamming pad for firm grip

## Slide 29: Engineering Design
Data when moving fingers
Signals when moving wrist
Signals when grabbing objects