## Slide 1: 3d-Printed Granular Jamming Hand
Melissa Indoe
Chris Kang
Sean Phelan
Maggie Serra
Chris Wallace

## Slide 2: Introduction
Project Objective
Problem Statement
Project Impact
Deliverables for Next Semester
All this belongs to Sean

## Slide 3: Project Review
In order for the project to meet all of the objectives stated, the team needed to design a prosthetic that mimicked a human hand in appearance, size, weight, and function
These criteria can be broken down into two main subsystems:
  3D printed fingers/palm/forearm
  granular jamming pad

## Slide 4: 3D Printed Segments
Fully functional fingers have already been designed, modeled, and manufactured
The palm has been modeled and is ready for manufacture
The team has decided to modify an existing open-source forearm housing
  This is because modeling curves in OpenSCAD can be complex
  Additionally, the forearm is not the focus of the project
Finger prototype demonstrating full range of motion.

## Slide 5: Finger and Palm
Iterative Design—The team has already developed a fully functional finger
Other parts of the design (mainly the palm), will require further iterations to come to a fully functional system

## Slide 6: Granular Jamming Pad
Aids with grasping small or irregularly shaped objects
Will consist of one pad on the palm of the hand
Pad will be made with silicon and filled with coffee grounds
  Silicon can easily be slip-cast to create irregular shapes
  Coffee grounds are cheap, readily available, and universally recognized as the most effective granular jamming material
When pressed around an object, the granules will be forced into a tightly packed arrangement by removing the air with a vacuum
This allows the pad to pick up objects that the fingers may not be able to manipulate

## Slide 7: Location/Attachment of Pad
Granular jamming pad will be glued into the palm housing
  Wire guides prevent the wire from snagging under the pad
Silicone grips will be glued to the flat surfaces of the fingers

## Slide 8: Engineering Design
Electrical Considerations—Chris Wallace
Control Considerations—Chris Kang
Safety Considerations—Sean

## Slide 9: Professional Drawings/Assembly Models
Maggie

## Slide 10: Gantt Chart

## Slide 11: Bill of Materials
Sean