## Slide 1: 3d-Printed Granular Jamming Hand
Melissa Indoe
Chris Kang
Sean Phelan
Maggie Serra
Chris Wallace

## Slide 2: Project Background
About 12,500 new arm amputations happen every year
  Most common reasons for arm amputation:
    Trauma (77%)
    Congenital (8.9%)
    Tumor (8.2%)
    Other diseases (5.8%)
Types of arm amputation:
  Transcarpal (Some of the fingers)
  Wrist Disarticulation
  Transradial
  Transhumeral
  Shoulder Disarticulation
  Forequarter Amputation

## Slide 3: Project Background (continued)
Mechanical hands have existed for years
  Run by cable attached to the shoulder
    Open/closed by shrugging
  Inaccurate motions
  Poor ability to grasp irregularly shaped objects
  Uncomfortable
  Expensive
Commercially available myoelectric hands have existed for the last 5-10 years
  Incredibly expensive
  Heavy
    2 to 3 times heavier than hook and cable
  Uncomfortable

## Slide 4: Problem Statement
Create an open-source, affordable and high functioning prosthetic hand
The hand should be task-oriented and able to achieve household activities requiring relatively low strength and high dexterity

## Slide 5: Societal Impact
Prosthetic
  Able to improve quality-of-life for thousands of upper limb amputees
  Affordable and approachable solution
Able to be used as hand analogs in hazardous situations
  Handling of hazardous materials
  Handling of babies in incubators
  Manufacturing and automation
Open source
  Able to be downloaded, edited and improved
  by anyone, anywhere.

## Slide 6: State-of-the-Art Designs
bebionic3 hand – used as human prosthesis
Individual Motors in each finger
  Positioned to optimize weight distribution, making the hand feel lighter and more comfortable.
14 Selectable grip patterns and hand positions
Proportional Speed Control
  precision control over delicate tasks, picks up an egg as easily as crushing an empty can.
Durable construction
  strong enough to handle up to 45kg
Selectable thumb positions
Soft finger pads to enhance grip

## Slide 7: State-of-the-Art Designs
i-limb ultra revolution – used as human prosthesis
Powered rotating thumb
Five independently articulating digits with individual stall out ability. Each finger bends at the natural joints
A variety of flexible wrist options enabling more natural movement
Remote electrodes are
waterproof, low profile,
and gold-plated for higher
sensitivity
Battery powered

## Slide 8: Existing Open-Source Designs
RoboHand
Completely 3D printed except for three components
Bend wrist down to close fingers
Bend wrist up to release grip
Designed for people with no fingers

## Slide 9: Existing Open Source Designs
InMoov
3D printed by a hobbyist
Uses motors and sensors

## Slide 10: Granular Jamming
Jamming –a physical process by which some materials, such as granular materials become rigid with increasing density.
Coarse substance in a flexible casing is soft until air is removed
  Example: Coffee grounds in a balloon
This can be used to pick up, grip, or throw objects
Notes: When particles are not jammed, they are able to flow past each other. When jammed, the group of particles becomes more rigid, like how sand can be poured, but is still able to support your weight when you stand on it.
The planned design will make use of this by having pads of granular material along the palm of the hand, and then forcing the granules to jam by sucking the air out of the sac.

## Slide 11: Granular Jamming In Action

## Slide 12: Conceptual Designs
To simplify the design process, brainstorming was split into categories:
  Category 1: Hand Ideas
    Ideas relating to the rigid components of the hand
  Category 2: Granular Jamming Ideas
    Ideas relating to the granular jamming pads
  Category 3: Other Considerations
    These were ideas or requirements that did not fit into any one category

## Slide 13: Hand Ideas
Joint ideas
  Ways to move joints
    Pneumatics
    Motors (one per joint)
    Cables
      One cable per finger
      One cable per finger, share cable for ring and pinky
      One cable per joint per finger
      One cable for 2 joints per finger
    Motors and cables (motors at finger base)
  Ideas to hold position
    Gear teeth at joint interface
    External joint locks

## Slide 14: Hand Ideas (continued)
Straightening out the hand
  Long rubber bands
  Dental rubber bands
  Flat springs
  A second set of cables
Sensing grip
  No grip sense: vacuum activated by button
  Place bump sensor under granular jamming pad
  Place encoder on servo motor, see if servo is stalled

## Slide 15: Joint Ideas Decision Matrix
Category: | Simplicity | Affordability | Size | Range of Motion | Totals:
Category Weight: | 10 | 8 | 10 | 8 | 
Item: |  |  |  |  | 
Pneumatics | 2 | 4 | 3 | 6 | 130
Motors (1/joint) | 1 | 1 | 1 | 10 | 108
Cables | 9 | 9 | 9 | 7 | 308
Motors & Cables | 6 | 7 | 5 | 8 | 230

## Slide 16: Cabling Ideas Decision Matrix
Category: | Simplicity | Affordability | Range of Motion | Totals:
Category Weight: | 10 | 8 | 8 | 
Item: |  |  |  | 
5 Cables (1/Finger) | 9 | 9 | 7 | 218
4 Cables | 9 | 10 | 5 | 210
1 Cable/Joint | 2 | 2 | 9 | 108
1 Cable/2 Joints | 4 | 4 | 8 | 136

## Slide 17: Hand Straightening Ideas Decision Matrix
Category: | Simplicity | Affordability | Reliability | Repairability | Range of Motion | Totals:
Category Weight: | 10 | 8 | 7 | 6 | 8 | 
Item: |  |  |  |  |  | 
Long Rubber Bands | 8 | 9 | 4 | 2 | 7 | 248
Dental Rubber Bands | 6 | 9 | 5 | 9 | 7 | 277
Flat Springs | 8 | 6 | 9 | 5 | 7 | 277
Second Set of Cables | 4 | 2 | 8 | 7 | 9 | 226

## Slide 18: Grip Sense Decision Matrix
Category: | Simplicity | Affordability | Reliability | Repairability | Usability | Totals:
Category Weight: | 10 | 8 | 7 | 6 | 10 | 
Item: |  |  |  |  |  | 
Vacuum Button | 9 | 9 | 9 | 9 | 1 | 289
Bump Sensor | 4 | 4 | 3 | 2 | 10 | 205
Encoder Boards | 8 | 8 | 8 | 8 | 9 | 338

## Slide 19: Granular Jamming Ideas
Granular Jamming Material
  Sand
  Coffee grounds
  Plastic stuffing materials
Housing Material
  Balloons
  Silicone
Layout
  Interconnected pads
    Pad for fingertip
    Pad for all three finger sections
    Pad for only fingertip and base sections
  Individual pads

## Slide 20: Housing Material Decision Matrix
Category: | Simplicity | Affordability | Feasability | Totals:
Category Weight: | 10 | 8 | 9 | 
Item: |  |  |  | 
Balloon | 8 | 10 | 7 | 223
Silicone | 9 | 9 | 8 | 234

## Slide 21: Connection Method Decision Matrix
Connecting jamming pads to vacuum
  Each pad has a tube to the vacuum
  Pads have connections to each other
Category: | Simplicity | Affordability | Feasability | Totals:
Category Weight: | 10 | 8 | 9 | 
Item: |  |  |  | 
Interconnected | 9 | 8 | 7 | 217
Individual | 5 | 6 | 3 | 125

## Slide 22: Preliminary Testing
To see which parts of the hands were most frequently used, some simple tests were conducted
Household items were coated in chalk and then manipulated
  This showed in chalk where the hand had contacted the object
Conclusion:
  Mainly the fingertips and palm were used
  This was then used to determine the value of individual granular jamming pads (i.e. which were most important to keep)
Other testing will also be done to determine the best granular jamming material

## Slide 23: Preliminary testing (continued)

## Slide 24: Layout Design Comparison
Layout of Granular Jamming Pads
Pad in each length
Pad in first and third length

## Slide 25: Layout Decision Matrix
Category: | Simplicity | Performance | Feasability | Totals:
Category Weight: | 10 | 9 | 9 | 
Item: |  |  |  | 
Pad for 1 | 9 | 5 | 7 | 198
Pad for 1,2,&3 | 6 | 8 | 5 | 177
Pads on 1 & 3 | 8 | 7 | 7 | 206

## Slide 26: Other Considerations
Polycarbonate plastic
  Making the product out of polycarbonate plastic means that it will be much stronger than most available 3d printed plastic
Use with touch screens
  Conductive fabric can be added to the index finger and thumb to allow its use with smartphones
Nails
  Nails are used for certain tasks (such as opening bottles)
  Adding prosthetic “nails” to the project will add a little functionality
Size
  Hand must follow roughly the same size of a real human hand, and cannot be much heavier

## Slide 27: Hand Size
Important to match size of an average hand
Hand segment lengths (middle finger):
  L1 = 44.6 mm
  L2 = 26.3 mm
  L3 = 17.4 mm
  Ltip = 3.95 mm
  Lpalm = 88.2 mm
Palm Width = 79 mm
Finger Width= 19.75 mm

## Slide 28: Hand size (continued)
Weight of the hand = 425.7 g
Weight of hand & forearm = 1,699.1 g
Finger length ratios:
  Index = 0.8*(Middle Length)
  Ring Length = 0.93*(Middle Length)
  Pinky Length = 0.74*(Middle Length)

## Slide 29: Conceptual Design
Primary hand design:
  Run by 5 cables attached to motors in the forearm
  Hand will be kept straight via dental rubber bands or flat springs
    (If there is time, both will be tested)
  Grip will be sensed via encoders tracking each motor
  Emulate the size and weight of an average human hand
Secondary goals:
  Wrist motion
  Locking joints
  Use with touchscreens
  Accurate finger length ratios
  Nails

## Slide 30: Technical Analysis
Real hand motion
3 degrees of freedom
  Supination/pronation
  Extension/flexion
  Ulnar deviation/radial deviation

## Slide 31: Technical Analysis
2 degrees of freedom
Twist and extension/flexion

## Slide 32: Engineering Design
Motors for fingers
A digital I/O for signals from sensors and motors
Granular jamming pad for firm grip

## Slide 33: Engineering Design
Data when moving fingers
Signals when moving wrist
Signals when grabbing objects

## Slide 34: Budget

## Slide 35: Deliverables at end of Semester
Gain significant knowledge in the materials and robotics field
OpenSCAD will be used to finalize design and create a complete prototype of the device in Phases II and III.
Finalized Bill of Materials
Understand and address the impact of the design in ethical, environmental, social, political, health and safety, sustainability, standardization/standards context
Complete technical analysis
Testing of designs and interfaces
Website design

## Slide 36: Gantt chart