## Slide 1: 3d-Printed Granular Jamming Hand
Melissa Indoe
Chris Kang
Sean Phelan
Maggie Serra
Chris Wallace

## Slide 2: Problem Statement
3 million population of arm amputees worldwide
  59% are below the elbow
Current prosthetic hands are costly
  Only half of arm amputees can afford prosthetic hands
  People in developing countries cannot get access to such device
There is a need to develop an affordable, readily available prosthetic hands

## Slide 3: Project Objective
Create an open-source, affordable, multifunctional, 3-D printed prosthetic hand
  Costs less than $500
  Able to perform a number of everyday tasks
  Designed such that consumer-level assembly is easy
  Open source
    Anyone can download the design from the internet and modify the hand to suit their own needs
Semester Objective
  Fabricate a working prototype

## Slide 4: Deliverables
Phase 5:
3D printed second iteration of complete hand
Continued programming for the Arduino Uno
Updated forearm model
Revamped and tested methods for granular jamming pad production
Revamped sensor setup
Obtained additional parts
Second printed iteration of full hand.

## Slide 5: Project Review
Granular Jamming Pad design and production plan were generated in Phase 4
  The production plan was to slip cast a latex pad using an ABS mold
Finger control was to be performed via sliding motors and Hall Effect sensors
  Springs would enable the motors to slide
  A magnet would be attached to each motor
  Hall effect sensors would be attached to the housing
  As the force increases, motors move, and sensors can be used to interpolate force
Granular jamming pad design.
Proposed Hall Effect sensor setup.

## Slide 6: Project Review
First palm iteration was printed in Phase 4
  It had several points of failure:
    Finger tolerance was too small
    Cable guides detached from palm surface
    Thumb bent incorrectly
Design changes were proposed
  Wire guides would be made shorter and with a modified cross section
  Thumb would be moved to a new position
First hand iteration (top), and first palm iteration displaying thumb issues (bottom).
Old vs new cable guard design and proposed hand design

## Slide 7: Programming Updates - Overview
Proof of concept
  Not using actual connections to a human – simulate with software.
Simulate user inputs
  Finger control
    Control motors
    Limit motor motion with potentiometer
  Granular Jamming
    Pump control
    Valve control

## Slide 8: Programming Updates - User Interface
GUIDE from MATLAB
  Easy for the user
  Toggle buttons to choose fingers
  Buttons to close or open fingers

## Slide 9: Programming Updates
Testing Setup
  Connecting to PC via USB
  Servos operating properly
  Testing potentiometer

## Slide 10: Programming Updates - Upcoming
What’s to come:
  Ability to stop motors with potentiometers
  Control of pump
  Control of valve
  Update GUI with options for pump and valve
  Connect to Arduino Uno via Bluetooth

## Slide 11: Palm Updates
As per Phase 4 design goals, a new version of the hand was made with repositioned thumb and redesigned cable guides
The new design also featured a slightly higher tolerance to eliminate bridging
This design was printed on March 4th
Some parts worked as expected and some posed new design problems
Old (top) and new (bottom) hand designs.

## Slide 12: Palm Updates
The thumb was moved to a position where it would meet with the middle finger upon tightening the cable
  This allows the hand to pick up small objects
The design differs slightly from the human hand
  The human hand typically uses the index finger to manipulate small objects
  However, putting the thumb at an angle meeting the index finger interferes with the forearm mount
  This difference should not interfere with day-to-day tasks
This aspect of the design worked as expected and displayed correct finger motion
Hand demonstrating desired motion.

## Slide 13: Palm Updates
The redesigned cable guides, however, did not work
This is because the hole for the cable had too small of a surface area for support material removal
  Support material is typically removed via an acid bath
  The cross section of the cable guide holes was too small for the acid bath to access the support material
  Therefore the cable guides are clogged and the cable guide design must be revisited
Solution: Add more surface area to cable guide holes
Cable guide holes are blocked with black support material

## Slide 14: Palm Updates
Current palm design:
  Holes have been added to allow acid to access support material
  Cable guides have again been made into a U shape, creating more surface area in the tunnel itself
  Thumb cable guide has been reconfigured into an “A” shape to create better leverage
Old (left) and new (right) palm designs

## Slide 15: Sensor Updates
Phase 4 sensor setup required motor slides
  This required a moving part in the forearm, adding complexity to the design
  Forearm design was already proving to be very complex and posed a problem keeping with project timelines
New sensor setup proposed: Springs and linear potentiometers
  These negate the need for motor slides
  They work on the same principle as the motor slides

## Slide 16: Sensor Updates
How the new sensor setup works:
  It takes a nominal force to reel in the finger
  When the finger makes contact, the force spikes
  A spring connecting two sections of cable stretches more under greater force
  Therefore, contact can be determined via spikes in spring position
This can be also used to determine exact force at the finger
  If the K value of the spring is known, force can be interpolated using Hooke’s law
  However, force calculation will not be within the scope of this project
    Requires conversion of logarithmic scale of the potentiometers to a linear change in distance

## Slide 17: Forearm Design
Originally planned to reuse InMoov forearm
  This proved difficult since the InMoov could not be imported into SolidWorks
Solution:
  Model forearm from scratch
Top case
  Hand mounting
  Arduino and shield mounting
Bottom Case
  Servo motor mounting

## Slide 18: Forearm Design – Moving Forward
Mounts must still be made for the following components:
  Pump
  Pneumatic valve
  Battery
  Sensors
It is possible that not everything will fit inside the forearm
  This is okay because this is a first prototype, proving that the concept works
  Future users may hone the design so that everything does fit

## Slide 19: Granular Jamming
Original Idea: Slip cast latex in a 3D printed mold
Current Idea: Use a glove as the casing
  Cut the fingers and cuff off, use the palm portion
  Use super glue to seal the edges
  Attempted using disposable latex, PVC, and nitrile gloves

## Slide 20: Granular Jamming
Disposable gloves showed promise to be airtight and were easy to construct. However there was concern about the durability of the gloves.
Solution: Reusable kitchen gloves
  Problems Encountered:
    The first set (yellow) were crumpled from being in the package, preventing them from forming an airtight seal.
    Since reusable gloves have a dedicated left and right glove, it was much harder to cut a large area to use

## Slide 21: Granular Jamming
Tried different gloves with a longer cuff and a cotton flock lining
Used the cuff instead of the palm of the glove
Able to secure the edges with glue (leaving a 1” opening)
  Inflated the glove and submerged it in water to look for leaks
  Bubbles indicated an air leak, so the glove was removed and the leak was fixed with more superglue, which made a successful airtight pocket.

## Slide 22: Website Updates
The website has been updated
Design changes:
  Totally new format
  New navigation
Content changes:
  Updated with all of the latest project work
Web address:
  http://granular3dhand.squarespace.com/

## Slide 23: Moving Forward
Hardware
  Finish forearm design
  Print hand and forearm
  Assemble hand and forearm
  Integrate granular jamming
  Assembly of electronics inside housing
Software
  Finish programming
    Integration of potentiometers
    Control of pump and valve
  Continue updating website

## Slide 24: Bill of Materials
Quantity | Part Purchased | Price
1 | Arduino Uno board REV3 | $28.57
1 | I/O expansion shield | $15.99
2 | Relay module V2 | $15.60
4 | MG995 metal servo | $9.52
1 | 12V expandable battery | $25.99
1 | 3/8" x 3/4" springs | $8.90
1 | Microbrushless air vacuum pump | $82.50
1 | Solenoid pneumatic valve | $49.95
1 | Arduino bluetooth dongle | $6.78
1 | Pneumatic tubing | $10.50
4 | Linear potentiometer | $43.61
 | Total Price: | $297.91

## Slide 25: Gantt Chart

## Slide 26: Construction/Testing Time Table