## Slide 1: 3d-Printed Granular Jamming Hand
Melissa Indoe
Chris Kang
Sean Phelan
Maggie Serra
Chris Wallace

## Slide 2: Project Background
About 12,500 new arm amputations happen every year
  Most common reasons for arm amputation:
    Trauma (77%)
    Congenital (8.9%)
    Tumor (8.2%)
    Other diseases (5.8%)
Types of arm amputation:
  Transcarpal (Some of the fingers)
  Wrist Disarticulation
  Transradial
  Transhumeral
  Shoulder Disarticulation
  Forequarter Amputation

## Slide 3: Project Objective
Create an open-source, affordable and high functioning prosthetic hand
The hand should be task-oriented and able to achieve household activities requiring relatively low strength and high dexterity
Major issues involved:
  Maintaining dexterity
  Keeping costs low
  Durability

## Slide 4: Societal Impact
Prosthetic
  Able to improve quality-of-life for thousands of upper limb amputees
  Affordable and approachable solution
Able to be used as hand analogs in hazardous situations
  Handling of hazardous materials
  Handling of babies in incubators
  Manufacturing and automation
Open source
  Able to be downloaded, edited and improved
  by anyone, anywhere.

## Slide 5: Current Solutions
Mechanical hands have existed for years
  Run by cable attached to the shoulder
    Open/closed by shrugging
  Inaccurate motions
  Poor ability to grasp irregularly shaped objects
  Uncomfortable
  Expensive
Commercially available myoelectric hands have existed for the last 5-10 years
  Incredibly expensive
  Heavy
    2 to 3 times heavier than hook and cable
  Uncomfortable

## Slide 6: State-of-the-Art Designs
bebionic3 hand – used as human prosthesis
Individual Motors in each finger
  Positioned to optimize weight distribution, making the hand feel lighter and more comfortable.
14 Selectable grip patterns and hand positions
Proportional Speed Control
  precision control over delicate tasks, picks up an egg as easily as crushing an empty can.
Durable construction
  strong enough to handle up to 45kg
Selectable thumb positions
Soft finger pads to enhance grip

## Slide 7: State-of-the-Art Designs
i-limb ultra revolution – used as human prosthesis
Powered rotating thumb
Five independently articulating digits with individual stall out ability. Each finger bends at the natural joints
A variety of flexible wrist options enabling more natural movement
Remote electrodes are
waterproof, low profile,
and gold-plated for higher
sensitivity
Battery powered

## Slide 8: Existing Open-Source Designs
RoboHand
Completely 3D printed except for three components
Bend wrist down to close fingers
Bend wrist up to release grip
Designed for people with no fingers

## Slide 9: Existing Open Source Designs
InMoov
3D printed by a hobbyist
Uses cables driven by motors for motion

## Slide 10: Granular Jamming
Jamming –a physical process by which some materials, such as granular materials become rigid with increasing density.
Coarse substance in a flexible casing is soft until air is removed
  Example: Coffee grounds in a balloon
This can be used to pick up, grip, or throw objects
Notes: When particles are not jammed, they are able to flow past each other. When jammed, the group of particles becomes more rigid, like how sand can be poured, but is still able to support your weight when you stand on it.
The planned design will make use of this by having pads of granular material along the palm of the hand, and then forcing the granules to jam by sucking the air out of the sac.

## Slide 11: Granular Jamming In Action

## Slide 12: Conceptual Designs
To simplify the design process, brainstorming was split into categories:
  Category 1: Hand Ideas
    Ideas relating to the rigid components of the hand
  Category 2: Granular Jamming Ideas
    Ideas relating to the granular jamming pads
  Category 3: Other Considerations
    These were ideas or requirements that did not fit into any one category

## Slide 13: Hand Ideas
Joint ideas
  Ways to move joints
    Pneumatics
    Motors (one per joint)
    Cables
      One cable per finger
      One cable per finger, share cable for ring and pinky
      One cable per joint per finger
      One cable for 2 joints per finger
    Motors and cables (motors at finger base)
  Ideas to hold position
    Gear teeth at joint interface
    External joint locks

## Slide 14: Hand Ideas (continued)
Straightening out the hand
  Long rubber bands
  Dental rubber bands
  Flat springs
  A second set of cables
Sensing grip
  No grip sense: vacuum activated by button
  Place bump sensor under granular jamming pad
  Place encoder on servo motor, see if servo is stalled

## Slide 15: Decision Matrices:
Category: | Simplicity | Affordability | Size | Range of Motion | Totals:
Category Weight: | 10 | 8 | 10 | 8 | 
Item: |  |  |  |  | 
Pneumatics | 2 | 4 | 3 | 6 | 130
Motors (1/joint) | 1 | 1 | 1 | 10 | 108
Cables | 9 | 9 | 9 | 7 | 308
Motors & Cables | 6 | 7 | 5 | 8 | 230
Category: | Simplicity | Affordability | Range of Motion | Totals:
Category Weight: | 10 | 8 | 8 | 
Item: |  |  |  | 
5 Cables (1/Finger) | 9 | 9 | 7 | 218
4 Cables | 9 | 10 | 5 | 210
1 Cable/Joint | 2 | 2 | 9 | 108
1 Cable/2 Joints | 4 | 4 | 8 | 136

## Slide 16: Decision Matrices (continued):
Category: | Simplicity | Affordability | Reliability | Repairability | Range of Motion | Totals:
Category Weight: | 10 | 8 | 7 | 6 | 8 | 
Item: |  |  |  |  |  | 
Long Rubber Bands | 8 | 9 | 4 | 2 | 7 | 248
Dental Rubber Bands | 6 | 9 | 5 | 9 | 7 | 277
Flat Springs | 8 | 6 | 9 | 5 | 7 | 277
Second Set of Cables | 4 | 2 | 8 | 7 | 9 | 226
Category: | Simplicity | Affordability | Reliability | Repairability | Usability | Totals:
Category Weight: | 10 | 8 | 7 | 6 | 10 | 
Item: |  |  |  |  |  | 
Vacuum Button | 9 | 9 | 9 | 9 | 1 | 289
Bump Sensor | 4 | 4 | 3 | 2 | 10 | 205
Encoder Boards | 8 | 8 | 8 | 8 | 9 | 338

## Slide 17: Conceptual Hand Design
Run by 5 cables attached to motors in the forearm
Hand will be kept straight via dental rubber bands or flat springs
  (If there is time, both will be tested)
Grip will be sensed via encoders tracking each motor

## Slide 18: Granular Jamming Ideas
Granular Jamming Material
  Sand
  Coffee grounds
  Plastic stuffing materials
Housing Material
  Balloons
  Silicone
Layout
  Interconnected pads
    Pad for fingertip
    Pad for all three finger sections
    Pad for only fingertip and base sections
  Individual pads

## Slide 19: Granular Jamming Decision Matrices
Category: | Simplicity | Affordability | Feasability | Totals:
Category Weight: | 10 | 8 | 9 | 
Item: |  |  |  | 
Interconnected | 9 | 8 | 7 | 217
Individual | 5 | 6 | 3 | 125
Category: | Simplicity | Affordability | Feasability | Totals:
Category Weight: | 10 | 8 | 9 | 
Item: |  |  |  | 
Balloon | 8 | 10 | 7 | 223
Silicone | 9 | 9 | 8 | 234
Housing Material
Connection for Pads

## Slide 20: Preliminary Testing
To see which parts of the hands were most frequently used, some simple tests were conducted
Household items were coated in chalk and then manipulated
  This showed in chalk where the hand had contacted the object
Conclusion:
  Mainly the fingertips and palm were used
  This was then used to determine the value of individual granular jamming pads (i.e. which were most important to keep)
Other testing will also be done to determine the best granular jamming material

## Slide 21: Preliminary testing (continued)

## Slide 22: Preliminary testing (continued)

## Slide 23: Preliminary testing (continued)

## Slide 24: Layout Design Comparison
Layout of Granular Jamming Pads
Pad in each length
Pads on 3 segments for index and middle

## Slide 25: Other Considerations
Polycarbonate plastic
  Making the product out of polycarbonate plastic means that it will be much stronger than most available 3d printed plastic
Use with touch screens
  Conductive fabric can be added to the index finger and thumb to allow its use with smartphones
Nails
  Nails are used for certain tasks (such as opening cans)
  Adding prosthetic “nails” to the project will add a little functionality
Size
  Hand must follow roughly the same size of a real human hand, and cannot be much heavier

## Slide 26: Hand Size
Important to match size of an average hand
Hand segment lengths (middle finger):
  L1 = 44.6 mm
  L2 = 26.3 mm
  L3 = 17.4 mm
  Ltip = 3.95 mm
  Lpalm = 88.2 mm
Palm Width = 79 mm
Finger Width= 19.75 mm

## Slide 27: Hand size (continued)
Weight of the hand = 425.7 g
Weight of hand & forearm = 1,699.1 g
Finger length ratios:
  Index = 0.8*(Middle Length)
  Ring Length = 0.93*(Middle Length)
  Pinky Length = 0.74*(Middle Length)

## Slide 28: Conceptual Design
Primary hand design:
  Run by 5 cables attached to motors in the forearm
  Hand will be kept straight via dental rubber bands or flat springs
  Grip will be sensed via encoders
  Granular jamming pads will be interconnected and housed in silicone
  Granular jamming pads will be placed with 3 pads/finger on the most active parts of the hand, 2 pads/finger elsewhere
  Emulate the size and weight of an average human hand
Secondary goals:
  Wrist motion
  Locking joints
  Use with touchscreens
  Accurate finger length ratios
  Nails

## Slide 29: Areas For Technical Analysis
Granular jamming housings and materials
  Physical tests of granular jamming pads to see what materials are most appropriate
Granular jamming requirements
  What is the minimum vacuum force needed for effective jamming
Forces on joints
  Design considerations needed to avoid snapping of the plastic
  Generate models to see if joint pins can be printed or should be metal
  Determine whether or not ABS or PLA plastics may be used

## Slide 30: Technical Analysis
Friction force
Joint force
mg
F(hand)
Friction force
Tension
Tension
Resisting force

## Slide 31: Engineering Design
Method
  1st : prototype so that software and device are ready. Then choose which sensor to measure signals from patients
Build and Test
  Duration of activating motors is to be tested as we build our prototype
  Periodically manufacture new prototypes for testing—iterative development
Granular jamming
  Fabrication/wear must be in consideration
  Housing and material have to be reliable and convenient for everyday use
Hand grip force
  Battery usage can be known for motors and vacuum for granular jamming system

## Slide 32: Budget
Part | Quantity | Cost | Total
dyIO | 1 | $75.00 | $75.00
Polycarbonate 3mm Filament | 1 | $74.99 | $74.99
Natural ABS 3mm Filament | 1 | 37.95 | $37.95
10 piece rotarty encoder set | 1 | 10 | $10
Servo Motor | 7 | 8.95 | $62.65
25 1/4th inch stainless steel screws | 1 | 6.49 | $6.49
30 pack Small Ball Bearings | 1 | 14.95 | $14.95
30 bag 5/16" rubber bands | 1 | 4.25 | $4.95
VEX Robotics NiMH Robot Battery | 1 | 19.99 | $19.99
6' Silicone Air Line Tubing | 1 | 3.33 | $3.33
1 pint Platex Mold Latex | 1 | 36 | $36.00
Detailed Plastic Acrylic based | 5 | 2.99 | $32.40
Air Pincette Vacuum Tweezers | 1 | 75 | $75.00
Total Price |  |  | $453.70

## Slide 33: Deliverables at end of Semester
OpenSCAD will be used to finalize design and create a complete prototype of the device in Phases II and III.
Complete technical analysis
Testing of designs and interfaces
Website design
Finalized Bill of Materials
Gain significant knowledge in the materials, robotics, and biomechanics fields
Understand and address the impact of the design in ethical, environmental, social, political, health and safety, sustainability, standardization/standards context

## Slide 34: Gantt chart