## Slide 1: 3d-Printed Granular Jamming Hand
Melissa Indoe
Chris Kang
Sean Phelan
Maggie Serra
Chris Wallace

## Slide 2: Project Background
About 12,500 new arm amputations happen in the US yearly
  The vast majority, (77%) are due to trauma
Amputation is a global problem
  It is estimated that only half of amputees ever get access to prosthetics
Existing myoelectric prosthetics start at $11,000
  This cost is completely prohibitive to many people
The most common form of arm amputation is transradial
  Incidence of about 44%
Loss of an arm can severely limit the independence of an amputee

## Slide 3: Project Objective
Create a “below-the-elbow” prosthetic hand
The hand should be:
  open-source, making it available to anyone anywhere
  highly affordable, making it inexpensive enough for anyone to use
  high-functioning, giving its owner back their independence in many day-to-day activities
  Task-oriented, focusing on dexterity rather than strength
Major issues involved:
  Durability
  Maintaining dexterity
  Keeping costs low

## Slide 4: Recap: Phase 1 Conceptual Design
Primary hand design:
  Run by 4 cables attached to motors in the forearm
  Kept straight via flat springs or dental rubber bands
  Grip will be sensed via encoders
  Granular jamming pads will be placed with 3 pads/finger on the most active parts of the hand, 2 pads/finger elsewhere
  Printed in polycarbonate plastic or possibly ABS
  Emulate the size and weight of an average human hand
  Printed joint pins
Notes: Primary hand design notes:
Run by 4 cables—initially it was to be run by 5 but this was simplified due to panel comments
Grip will be sensed via encoders—initially it was thought that the encoders would be necessary to maintain accuracy, this will be addressed later

## Slide 5: Major Areas of Concern
Printed joint pins
  Are they strong enough?
  Are they within the abilities of an average 3D printer?
Material
  Is ABS plastic strong enough for this application or is polycarbonate necessary?
Granular jamming pads
  Is granular jamming helpful enough to justify?
  Is there enough surface area for improved grip?
  Can we achieve a vacuum in a reasonable timeframe?

## Slide 6: Model for Technical Analysis
A basic model was generated in OpenSCAD
This model included:
  Finger segment lengths
  Joint pin size
  Hinge placement
Through examination, certain “common sense” design adjustments were made
  It was decided at this point to use rubber bands rather than flat springs
  This was because displacement at the joint interface was quite large
Notes: As another “Common sense” adjustment, the encoders were eliminated because it was clear that the fingers would not need that level of percision

## Slide 7: Technical Analysis—Joint Pin Stress
This model was then imported into Solidworks
Force studies were run on individual finger segments
Under standard working conditions, joint pin stresses never approached yield stress
  Yield stress of ABS: 44 MPa
  Maximum stress under working conditions: 13.8 MPa
  Factor of Safety: 3.2
Analysis of “FingerTip” segment

## Slide 8: Terms of the Joint Pin Stress Analysis
Material: ABS plastic
Force: 4.5 N
  The maximum force incurred by the selected servos
Fixed position: the joint pins
  Pulling the wire inward grinds the joint pins against the hinge
Force application:
  The point of connection at the fingertip
  The joint holes and wire guides elsewhere
Diagram of force application (purple) and fixed position (green) of finger segments

## Slide 9: Joint Pin Stress Analysis (continued)
Top Left:
Analysis of “FingerMid” segment
Top Right:
Analysis of “FingerBase” segment
Bottom Left:
Detail of stress concentration at the joint pin interface

## Slide 10: Joint Pin Analysis (Continued)
The joint pin analysis showed that ABS passed with flying colors
Therefore the idea of printing the project in polycarbonate plastic could be eliminated
  Although polycarbonate is much stronger, it requires a specialized extruder to print correctly
  It is also far more expensive than either ABS or PLA
This also suggested testing the joints with PLA plastic
PLA also passed these tests
  Yield stress of PLA: 47.8 MPa
  Maximum stress under working conditions: 13.8 Mpa
  Factor of Safety: 3.5

## Slide 11: Additional Solidworks Analysis
In an attempt to differentiate more between PLA and ABS plastics, two additional tests were run:
  First, a drop test, since it was very realistic that something designed to be used and removed often might fall
  Second, a test of ultimate strength, to see what worst-case conditions the hand could endure
Terms of these analyses:
  Drop test:
    Dropped from 1.5 meters high on a simulated concrete floor (worst case scenario)
  Load to Failure test:
    Two tests were run here:
      Worst case scenario: all force is transferred to joint pins
      Realistic scenario: force is transmitted to joint pins and top edge

## Slide 12: Solidworks Drop Tests
ABS incurred a maximum stress of 33.2 MPa, just 11 MPa short of failure
PLA incurred a maximum stress of 50.6 MPa, which was larger than its yield strength, 47.8 MPa
Conclusion: ABS gets a narrow pass and PLA fails
“FingerTip” drop test with ABS (top) and PLA (bottom)

## Slide 13: Terms of Load to Failure
Situation: Bending finger backward
  Bending it forward would only push it into the palm, which would protect it from damage
Force application:
  Through the joint pin holes (up and back)
Definition of “Failure”
  Applied stress is greater than yield strength
Pins were analyzed at base only
Two tests were run for each material
  “Worst case scenario”—force is only applied to joint pins
  “Realistic scenario”—joint pins elastically deform and the top edges make contact with other hinge
Worst case (top) and realistic case (bottom) diagrams of force application (purple) and fixed position (green)
Notes:   “Applied stress is greater than yield strength” was chosen because if the joint pins are bent, then they are useless (they don’t just have to be sheared off)
  Pins were analyzed at base only because base incurs the largest stress due to the fact that it has the whole finger acting as a moment arm

## Slide 14: Solidworks Load to Failure
In worst case scenario, both materials failed at just under 15 N
In realistic scenario, ABS failed at ~40 N, and PLA failed at ~43 N
In this test, both materials are comparable
Conclusion: Both materials are passable, but ABS is better (due to passing the drop test)
Worst case (left) and realistic (right) loading scenarios.

## Slide 15: Next Point of Analysis—Manufacturability
This design requires printing of floating joint pins
  If the fingers are to be printed in one piece as a non-assembly model, there is no way around floating joint pins
  This is extremely problematic because the printer must lay filament in midair with no support—anything manufactured this way will be warped.
  Therefore it is necessary to see if the warping of the joint pins is acceptable, or if another design must be found
One other major aspect of printing an articulated non-assembly model is that it has to have proper clearances
  If clearances are incorrect the model will fuse together

## Slide 16: Manufacturability
To test manufacturability of the finger, a test print of the model was performed
  Part of the draw of 3D printing is that material is extremely cheap and readily accessible
    This means that a project like this can be printed at an early stage, dealing with many manufacturing issues early on
  This print weighed 27 grams (well within limits for a human finger)
  It cost about 33 cents in material
  It took only 30 minutes to create (well within reasonable time constraint for prosthetic manufacture)
Model display in the Repetier software (left) and model in the process of printing (right)

## Slide 17: Manufacturability
Points of failure were identified
  Tolerances were too small
    Hinges were fused
  Joint pins were too warped for the design to function
Positive points were also identified
  Rubber band guide overhangs printed successfully
  Wire guide functioned with no issues
  Scaling was perfect
Notes: Tolerance was set to .5, well above the .04 mm that 3d printers should be capable of, but of course real life often isn’t like simulations.
To be fair part of this is the quality of the plastic here. This plastic was extruded at too high a temperature, which accounts for a lot of the “goopy” appearance (as well as some of the slop in the dimensions)

## Slide 18: Manufacturability—The Bad
Joint pins are definitely too rough for a plastic-on-plastic joint interface as was originally planned
Joint tolerance has been set too low, plastic has bridged the points of articulation and the finger is solid.

## Slide 19: Manufacturability—The Good
The scaling (left), rubber band guides (center) and wire guides (right) are all correct and functional.

## Slide 20: Manufacturability—What does it mean?
Based on these findings it should be completely reasonable to use 3D printing as the method of manufacture
It is more than possible to achieve the necessary detail at the needed scale (with some modification)
Modifications required:
  Larger joint clearances
  Avoid joint pin on plastic contact

## Slide 21: Manufacturability—Solution
Joint clearance was greatly increased
Bearings were introduced in order to solve the problem of warped joint pins
  The plastics involved are very pliable (especially when hot)
  Applying a heat gun and then press-fitting a bearing into the joint will solve all friction issues
  A clearance the size of a bearing (2mm) between parts will never bridge or fuse
Left to right: Improved joint clearances, bearings, bearing clearance.

## Slide 22: Technical Analysis: Granular Jamming Tests
I NEED CHRIS WALLACE AND CHRIS KANG’S TESTS TO WRITE THIS

## Slide 23: Addressing Major Areas of Concern
Printed joint pins
  Are they strong enough? YES
  Are they within the abilities of an average 3D printer? Yes, with bearings
Material
  Is ABS plastic strong enough for this application or is polycarbonate necessary? ABS is fine, PLA is also suitable
Granular jamming pads
  Is granular jamming helpful enough to justify? ???
  Is there enough surface area for improved grip? ???
  Can we achieve a vacuum in a reasonable timeframe? ???

## Slide 24: Review: Phase 2 Conceptual Design
Primary hand design:
  Run by 4 cables attached to motors in the forearm
  Kept straight via dental rubber bands
  Grip will be sensed via servos
  Granular jamming pads will be placed on the palm only
  Printed in ABS
  Emulate the size and weight of an average human hand
  Printed joint pins (as long as bearings are present)

## Slide 25
MELISSA I AM NOT SURE WHERE YOU WANT YOUR ANALYSIS SO JUST PUT IT IN WHERE YOU THINK IT’S MOST APPROPRIATE