## Slide 1: 3d-Printed Granular Jamming Hand
Maggie Serra
Chris Wallace
Melissa Indoe
Sean Phelan
Chris Kang

## Slide 2: Conceptual Designs
To simplify the design process, brainstorming was split into categories:
  Category 1: Hand Ideas
    Ideas relating to the rigid components of the hand
  Category 2: Granular Jamming Ideas
    Ideas relating to the granular jamming pads
  Category 3: Other Considerations
    These were ideas or requirements that did not fit into any one category

## Slide 3: Hand Ideas
Joint ideas
  Ways to move joints
    Pneumatics
    Motors (one per joint)
    Cables
      One cable per finger
      One cable per finger, share cable for ring and pinky
      One cable per joint per finger
      One cable for 2 joints per finger
    Motors and cables (motors at finger base)
  Ideas to hold position
    Gear teeth at joint interface
    External joint locks

## Slide 4: Hand Ideas (continued)
Straightening out the hand
  Long rubber bands
  Dental rubber bands
  Flat springs
  A second set of cables
Sensing grip
  No grip sense: vacuum activated by button
  Place bump sensor under granular jamming pad
  Place encoder on servo motor, see if servo is stalled

## Slide 5: Joint Ideas Decision Matrix
Category: | Simplicity | Affordability | Range of Motion | Totals:
Category Weight: | 10 | 8 | 8 | 
Item: |  |  |  | 
Pneumatics | 2 | 4 | 6 | 100
Motors (1/joint) | 1 | 1 | 10 | 98
Cables | 9 | 9 | 7 | 218
Motors & Cables | 6 | 7 | 8 | 180

## Slide 6: Cabling Ideas Decision Matrix
Category: | Simplicity | Affordability | Range of Motion | Totals:
Category Weight: | 10 | 8 | 8 | 
Item: |  |  |  | 
5 Cables (1/Finger) | 9 | 9 | 7 | 218
4 Cables | 9 | 10 | 5 | 210
1 Cable/Joint | 2 | 2 | 9 | 108
1 Cable/2 Joints | 4 | 4 | 8 | 136

## Slide 7: Hand Straightening Ideas Decision Matrix
Category: | Simplicity | Affordability | Reliability | Repairability | Range of Motion | Totals:
Category Weight: | 10 | 8 | 7 | 6 | 8 | 
Item: |  |  |  |  |  | 
Long Rubber Bands | 8 | 9 | 4 | 2 | 7 | 248
Dental Rubber Bands | 6 | 9 | 5 | 9 | 7 | 277
Flat Springs | 8 | 6 | 9 | 5 | 7 | 277
Second Set of Cables | 4 | 2 | 8 | 7 | 9 | 226

## Slide 8: Grip Sense Decision Matrix
Category: | Simplicity | Affordability | Reliability | Repairability | Usability | Totals:
Category Weight: | 10 | 8 | 7 | 6 | 10 | 
Item: |  |  |  |  |  | 
Vacuum Button | 9 | 9 | 9 | 9 | 1 | 289
Bump Sensor | 4 | 4 | 3 | 2 | 10 | 205
Encoder Boards | 8 | 8 | 8 | 8 | 9 | 338

## Slide 9: Granular Jamming Ideas
HI CHRIS

## Slide 10: Other Considerations
Polycarbonate plastic
  Making the product out of polycarbonate plastic means that it will be much stronger than most available 3d printed plastic
Use with touch screens
  Conductive fabric can be added to the index finger and thumb to allow its use with smartphones
Nails
  Nails are used for certain tasks (such as opening bottles)
  Adding prosthetic “nails” to the project will add a little functionality
Size
  Hand must follow roughly the same size of a real human hand, and cannot be much heavier

## Slide 11: Hand Size
Important to match size of an average hand
Hand segment lengths (middle finger):
  L1 = 44.6 mm
  L2 = 26.3 mm
  L3 = 17.4 mm
  Ltip = 3.95 mm
  Lpalm = 88.2 mm
Palm Width = 79 mm
Finger Width= 19.75 mm

## Slide 12: Hand size (continued)
Weight of the hand = 425.7 g
Weight of hand & forearm = 1,699.1 g
Finger length ratios:
  Index = 0.8*(Middle Length)
  Ring Length = 0.93*(Middle Length)
  Pinky Length = 0.74*(Middle Length)

## Slide 13: Conceptual Design
Primary hand design:
  Run by 5 cables attached to motors in the forearm
  Hand will be kept straight via dental rubber bands or flat springs
    (If there is time, both will be tested)
  Grip will be sensed via encoders tracking each motor
  Emulate the size and weight of an average human hand
Secondary goals:
  Wrist motion
  Locking joints
  Use with touchscreens
  Accurate finger length ratios
  Nails